## Slide 1: CAN Interface
Wang Hyunho
2021-06-30

## Slide 2: CAN Interface
Control Board
Driver Board
Driver Board
Driver Board
요약
  Step motor 구동을 위한 Control Board와 Driver Board 간 Can Interface 구현
  진행 내용
    Control Board, Driver Board 각각 Can Interface 구현 및 테스트
    Control Board와 Driver Board를 1:N 연결 테스트 진행
    신호 감쇄 확인 및 보드 수정 (33옴->0옴), 수정 완료
    송수신 테스트 완료
  H/W 및 CAN 구성
 | Control Board | Driver Board
MCU Part Name | STM32F429II | STM32F103RE
MCU System Clock | 144MHz | 8MHzU
Used CAN | CAN2 | CAN1
CAN Mode | Slave Mode | Master Mode
Baud rate | 500Kbps | 500Kbps

## Slide 3: CAN Interface
Project 구성
User files
Backup file
Backup file
Driver board
Control board

## Slide 4: CAN Interface
Group | Control Board | Driver Board | Type | Description | File
CAN | CAN* can; | CAN* can; | Extern pointer | can->xxx() | can.h, can.c
CAN | CanSetIntr0 CanResetIntr0 | CanSetIntr0 CanResetIntr0 | Function | Rx Interrupt Flag 설정 및 리셋 | can.h, can.c
CAN | CanInit() | CanInit() | Function | CAN Library 초기화 | can.h, can.c
CAN | CanConfig() | CanConfig() | Function | CAN alternate function 구성 | can.h, can.c
CAN | CanSend(…) | CanSend(…) | Function | CAN TX 전송 | can.h, can.c
BSP | UserClockSetting() | - | Function | STM32F429II의 PLL Clock 설정 144MHz | f429bsp.h, f429bsp.c
BSP | BspInit() | BspInit() | Function | Board support packet 초기화 | fxxxbsp.h, fxxxbsp.c
BSP | SetTimer0() ResetTimer0() | SetTimer0() ResetTimer0() | Function | Timer Interrupt Flag 설정 및 리셋 | fxxxbsp.h, fxxxbsp.c
BSP | LedInit() | LedInit() | Function | LED 초기화, Control 2개, Driver 1개 | fxxxbsp.h, smd.c
BSP | TimerInit() | TimerInit() | Function | 50ms interval timer interrupt 생성 | fxxxbsp.h, fxxxbsp.c
Major Functions

## Slide 5: CAN Interface
Driver Board 동작 설명
초기화
Timer Interrupt (50ms)
SW 1 확인
후, TX 전송
(송신 StdId = 0x32)
Can Rx Interrupt 처리
(수신 StdId = 0x31)

## Slide 6: CAN Interface
Control Board 동작 설명
초기화
Timer Interrupt (50ms)
50ms 마다 전송
(송신 StdId = 0x31)
Can Rx Interrupt 처리
(수신 StdId = 0x32)